## Slide 1: Getting to grips with Vitis
Adam Taylor

## Slide 2: What is Vitis
Vitis is unified software development environment from Xilinx
Offers Unified edge and cloud development methodologies
Support embedded and accelerated flows

## Slide 3: Vitis AI Development Environment
Vitis AI enables acceleration of AI inference at edge & Cloud
Supports leading frameworks such as TensorFlow, Caffe and Pytorch
Works with fixed point representation and Xilinx Deep Learning Processor Unit

## Slide 4: Vitis Accelerated Libraries
Several Open Source acceleration ready libraries
Common Libraries – offer a set of common functionality
Domain specific libraries – offer out of the box functions for specific domains e.g. vision

## Slide 5: Vitis Core Development Kit
GUI & Command line tools for compilation, debug and analysis of C, C++ and OpenCL designs.
Can use preferred GUI or integrated GUI
Supports embedded and accelerated flows

## Slide 6: Vitis Target Platforms
Embedded
  SoC – MPSoC, RFSoC, Zynq
  FPGA – MicroBlaze
Cloud – Alveo / AWS F1 Instance
Embedded SoC and Cloud applications can use acceleration flow.
All required files and boot elements are generated

## Slide 7: Xilinx Runtime library
Xilinx Runtime library (XRT) enables communication between the host and accelerator
Cloud based – Host x86
Embedded – Arm A9 or A53
Provides all libraries, APIs, drivers and utilities.

## Slide 8: Xilinx Runtime library
Key Functions of the Runtime include
Downloading the FPGA binary
Memory Management between Host and Accelerator
Execution Management
Board Management

## Slide 9: Element of Vitis
All projects required a platform
  Hardware element – makes available AXI connections, clocks and Interrupts in the PL to Vitis Compiler
  Software element – provides boot, XRT and QEMU support
  Linux element – FS, Image and SysRoot

## Slide 10: Vitis Output
Compiled binary (host) and XCLbin (accelerator)
Embedded System Output
  SD Card Image
    Image
    File System
    Binary and XCLBin
Cloud output
  Binary and XCLBin

## Slide 11: Vitis Development Flow
Software Emulation – Syntax errors & algorithm verification
Hardware Emulation – Optimize Performance, Interfacing & Resources

## Slide 12: OpenCL Framework
An open industry standard
For parallel computing
Of heterogeneous systems
Enables cross-platform functional portability
No code changes
Portable across CPU, GPU, FPGA, DSP, etc.
  Can run on cell phones, laptops, super computers
Important: No performance portability
Wide market adoption
Support implemented by
  Apple, AMD, Xilinx, Intel, ARM, Nvidia, Qualcomm, etc.
Many companies developing applications
  Image, video, audio processing, scientific calculations, medical imaging, and more
1-
9
Notes: An open industry standard for parallel computing: ˃ OpenCL C language ˃ OpenCL API ˃ OpenCL run time The OpenCL framework standard is maintained by Khronos Group (khronos.org).

## Slide 13: OpenCL Framework
Platform model
Defines representation of ANY platform
Contains
  Single host
  One or more OpenCL devices (compute device)
1-
1
1
Notes: OpenCL platforms are defined by the grouping of a host processor and one or more OpenCL computing devices. The host processor, which runs the OS for the system, is also responsible for the general bookkeeping and task launch duties associated with the execution of OpenCL applications. The device is the hardware element in the system on which the computing kernels of an OpenCL application are executed.

## Slide 14: OpenCL Framework
Platform model
Defines representation of ANY platform
Contains
  Single host
  One or more OpenCL devices (compute device)
Execution model
OpenCL application: Two parts
Host program
  Manages the entire application: OpenCL APIs
Kernels (OpenCL C language)
  Functions to accelerate, run on OpenCL devices
1-
1
2
Notes: Execution has two parts: ˃ Host program: runs on x86. ˃ Kernel: contains functions to accelerate and runs on OpenCL devices.

## Slide 15: OpenCL Framework
Platform model
Defines representation of ANY platform
Contains
  Single host
  One or more OpenCL devices (compute device)
Execution model
OpenCL application: Two parts
Host program
  Manages the entire application: OpenCL APIs
Kernels (OpenCL C language)
  Functions to accelerate: run on OpenCL devices
V++

## Slide 16: Execution Model – Command Queues
Interaction between host and device occurs via command queues
Created by host
Attached to a single device
  Note: Multiple command queues can be active within context
Three command types
Kernel execution commands
Memory commands
  Transfer data between host and different memory objects
Synchronization commands
  Put constraints on in the order in which commands are executed
1-
1
1
142337**slide

## Slide 17: Memory Model
Three types of memory objects
Buffer objects
  Contiguous block of memory
  Available to kernels for read/write
  Programmer can write data to buffers
  Access to data via pointers
Image objects (not a part of embedded profile)
  Hold images only
  Storage/format can be optimized for specific OpenCL device
  OpenCL framework provides functions to manipulate images
Pipes
  Data organized as FIFO
  Accessed (read/write) via built in
  Pipe not accessible from the host
1-
1
2
142340**slide

## Slide 18: Five Sub-regions of Memory Objects
Host memory
Visible to host only
OpenCL framework only defines how host memory interacts with OpenCL objects
Global memory
Visible to host and device
All work items in all workgroups can read/write there
Global on-chip memory – visible to device only
Constant memory
Region of global memory
Work items – read access only
Local memory
Local to workgroup (shared by all work-items in a group)
Private memory
Accessible by a work-item
1-
1
3
142343**slide

## Slide 19: Optimization
Optimization Possible at both Host and Kernel
Enables most responsive solution
Host optimization
Kernel optimization possible in OpenCL and C/C++
  Optimization Syntax differs

## Slide 20: Host Optimization
Optimize the data movement in the application before optimizing computation
Compute Unit Scheduling
  Multiple In-Order Command Queues
  Single Out-of-Order Command Queue
Notes: In the OpenCL API, all data is transferred from the host memory to the global memory on the device first and then from the global memory to the kernel for computation. The computation results are written back from the kernel to the global memory and lastly from the global memory to the host memory

## Slide 21: Host Optimization
Multiple In-Order Command Queues
Single Out-of-Order Command Queue

## Slide 22: Kernel Optimization – Data Types
Avoid native C data types e.g. int, float, double
Best performance is using bit accurate types (C/C++ Kernels)
  Arbitrary Precision Integer
  Arbitrary Precision fixed point
Enables smaller & faster logic implementations

## Slide 23: Kernel Optimization – Interfacing
Two types of data transfer
  Data Pointers via global memory (M_AXI)
  Scalar direct to kernel (AXI_LITE)
Vitis automatically selects interface type
Max data width is 512 bits – maximum performance leverages this

## Slide 24: Kernel Optimization – Pipelining
By default, every iteration of a loop only starts when the previous iteration has finished
Pipelining the loop executes subsequent iterations in a pipelined manner

## Slide 25: Kernel Optimization – Unrolling
Unrolling a loop enables the full parallelism
Full or Partial Unroll
Data dependencies in loops can impact the results of loop pipelining or unrolling

## Slide 26: Kernel Optimization – DataFlow
Improve kernel performance by enabling task-level pipelining
Be careful of
Single producer-consumer violations.
  Bypassing tasks.
  Feedback between tasks.
  Conditional execution of tasks.
  Loops with multiple exit conditions or conditions defined within the loop

## Slide 27: Kernel Optimization – Memory
Limited BRAM access bandwidth, can heavily impact the overall performance
Ability to partition and reshape arrays can increase bandwidth
Partition – Separates into different BRAMS
Reshape – allows combination of words

## Slide 28: Kernel Optimization - Pragmas
Optimization | C/C++ | OpenCL
Pipeline | #pragma HLS PIPELINE | __attribute__((xcl_pipeline_loop))
Unroll | #pragma HLS UNROLL | __attribute__((opencl_unroll_hint))
DataFlow | #pragma HLS DATAFLOW | __attribute__ ((xcl_dataflow))
Memory | #pragma HLS ARRAY_PARTITION | 
Further information can be found at
https://www.xilinx.com/html_docs/xilinx2020_1/vitis_doc/optimizingperformance.html#fhe1553474153030

## Slide 29: Vitis GUI – Project Settings

## Slide 30: Vitis GUI – Project Setting

## Slide 31: Vitis-Debug
Can Debug
  Software Emulation
  Hardware Emulation
Hardware flow insert ILA
Debugging will use QEMU and Logic Simulator

## Slide 32: Hands On Labs